## Slide 1
Presented by Eliot Mayer, W1MJ
Waltham Amateur Radio Association
September 27, 2023
W1MJ Fox Design
W1MJ Second-Generation Fox

## Slide 2
What is a Fox?
W1MJ FOX2 Design Goals
Design Overview
Fox Circuit Board Design
Software Design
Lessons Learned
Workshop Outline

## Slide 3
Some radio amateurs participate in hidden transmitter hunts for fun or for training, preferably both.
What is a Fox?
Serious Fun!
K1PJW finds joy in locating W1MJ’s Fox
Hidden transmitter hunts are sometimes called fox hunts. The fox is the hidden transmitter. It could be a radio ham hiding in the woods, but these days is more frequently an automated transmitter.

## Slide 4
First-generation fox used an MP3 player with a very simple interface to a Baofeng radio.
Design Goals, W1MJ FOX2
Goals for second-generation fox:
Longer deployments by going to sleep at night or transmitting on demand
Announce battery voltage
Stop transmitting when battery is low

## Slide 5
Design Overview
Block Diagram, W1MJ FOX2

## Slide 6
Case: Pelican 1200 Black
Battery: 12.8V 30AH LiFePO4
Radio: Baofeng UV-5R
Battery Eliminator: Baofeng Tech BL-5
Circuit Board
Design Overview
Main Components

## Slide 7
Case: Harbor Freight 0.30 Cal Ammo Box
Has Power Switch
Has Fuse
Baofeng F8HP Radio
12V 15AH Lead Acid Battery
DZS Elec Voltage Regulator
Design Overview
K1MJC’s Fox Assembly

## Slide 8
Design Overview
Heard about it at a QSO Today Expo tech forum
Capable of implementing the design goals
Low power consumption: 5V x 26 mA = 130 mW
Small: 51 x 21 mm
Inexpensive: $4
Why Raspberry Pi Pico?

## Slide 9
Fox Circuit Board Design

## Slide 10
Fox Circuit Board Design
Schematic: Altium Designer
PCB Layout: Altium Designer
Fabrication: Digi-Key DKRed

## Slide 11
Python is popular, easy to use, and free. I had taken a course.
CircuitPython has everything needed for this fox, including an MP3 decoding function.
Python is actually named after Monte Python’s Flying Circus!
Software Design
Usage of Pico’s 2MB Storage
Why CircuitPython?
20 files,
16 ksps mono

## Slide 12
Software Design
Program Outline
Import modules
Settings (message interval, start & stop times, etc)
Define Functions
Initialization
  IO Port assignments
  Miscellaneous initialization tasks
Set time (buttons, voice feedback via radio)
Buttons: Hour, Min (5-min increments), Run (long push for On Demand Mode)
Message Loop
  During scheduled time, with OK battery voltage
    Transmit all messages sequentially
    Measure and transmit battery voltage
    Repeat
  In On Demand Mode, wait for new request

## Slide 13
Software Design
Coding and Debugging: Mu Editor

## Slide 14
Software Design
Coding and Debugging: Visual Studio Code

## Slide 15
Don’t Assume
Use of AI – Caveat Emptor
Lessons Learned
Linear Regulator in K1MJC’s Battery Eliminator
Switching Regulator in Baofeng BL-5 Battery Eliminator
From OpenAI / ChatGPT
Adafruit page found with Google

## Slide 16
Don’t Assume
Use of AI – Caveat Emptor
Lessons Learned
Response to Reworded Question

## Slide 17
Don’t Assume
Use of AI – Caveat Emptor
It’s always something!
Lessons Learned
Original UV-5R
New UV-5R

## Slide 18
Northeast Massachusetts Fox Hunters
  https://groups.io/g/NEMassFoxHunters/messages
Prospect Hill Intermod, Winter 2022
  http://walthamara.org/phi/2022-winter.pdf
Google
  https://www.google.com/search?q=Hidden+Transmitter+Hunting
Fox Hunting References

## Slide 19
Thank You
w1mj.com/fox